## Slide 2
Course Code: EECE- 434
Course Name: Microwave Engineering Laboratory
Group No: 04

## Slide 3
PROJECT
Yagi-Uda Antenna Using CST Studio Suite

## Slide 4
GROUP MEMBERS
Name | Student ID
Mayan Uddin Sizan | 202016069
Mansib Hasan | 202116037
Md. Farhan Fuad | 202116046
Md. Mostaque Mahbub Tamim | 202116050
Nasif Ahmed Rafe | 202116072

## Slide 5
CONTRIBUTION
Student ID | Antenna Design | Parameters Adjustment | Result Analysis | Report Writing | Presentation Slides
202016069 |  |  |  |  | 
202116037 |  |  |  |  | 
202116046 |  |  |  |  | 
202116050 |  |  |  |  | 
202116072 |  |  |  |  | 

## Slide 6
Literature Review
Methodology
Introduction
Problem Statement and Design Criteria
SCOPE
Simulation Results
Interpretation of Results
Application of the Design
Shortcoming/Drawbacks of the Design
Conclusion
References

## Slide 7
Introduction
The Yagi-Uda antenna, known for its directionality and high gain, is a staple in wireless communication. Its unique design, featuring a driven element, reflector, and multiple directors, allows it to focus energy in a specific direction, enhancing signal reception and transmission over long distances. This antenna's adaptability and efficiency have cemented its place as a preferred choice in various applications, from amateur radio to space communication systems.

## Slide 8
Problem Statement and Design Criteria
Design, simulate and analyze Yagi-Uda antennas with 3 and 8 elements uing CST Suite. The objective is to evaluate the impact of the number of elements on key antenna parameters such as S parameter, VSWR, gain, and far-field polar diagram. The aim is to enhance antenna performance for efficient directional communication systems.

## Slide 9
Problem Statement and Design Criteria
Design criteria are as follows:
Frequency range
Element configuration
Simulation parameters
Performance metrics
Optimization

## Slide 10
Literature Review
This review covers Yagi-Uda antenna design, performance factors like director number and spacing, and CST-based optimization trends. Invented by Uda and Yagi, the antenna’s gain increases with more directors, though larger designs may be impractical for compact devices . A Yagi-Uda antenna has a dipole-driven element, and parasitic reflectors and directors, which passively shape the radiation pattern. Varying director lengths improves gain and impedance matching across frequencies .

## Slide 11
Element | 3 element Yagi-Uda antenna | 8 element Yagi-Uda antenna
Operating frequency | 2.45 GHz | 2.45 GHz
Wavelength | 113.2 mm | 113.2 mm
Dipole length | 0.5λ | 0.5λ
Reflector length | 0.55λ | 0.55λ
Director 1 length | 0.45λ | 0.45λ
Director 2 length | - | 0.4λ
Director 3 length | - | 0.35λ
Director 4 length | - | 0.35λ
Director 5 length | - | 0.35λ
Director 6 length | - | 0.35λ
Dipole to reflector spacing | 0.35λ | 0.35λ
Dipole to director spacing | 0.2λ | 0.2λ
Director to director spacing | 0.125λ | 0.125λ
Boom length | 0.75λ | 1.125λ
Table-1: Parameter values
Design parameters

## Slide 12
Flow Chart

## Slide 13
SIMULATION RESULTS
3 Element Yagi Uda Antenna
Fig: Diagram of three element Yagi-Uda Antenna

## Slide 14
S parameter(Before Sweeping)
Fig: S parameter at lambda value of 150

## Slide 15
Parametric Sweeping

## Slide 16
S parameter at 2.45 cutoff frequency

## Slide 17
VSWR

## Slide 18
Fig: Far-field analysis
Far-field
The maximum far field gain achieved is 7.837 dB.

## Slide 19
Fig: Gain vs Frequency curve
Gain vs Frequency

## Slide 20
Fig: Diagram of Eight element Yagi-Uda Antenna
Eight element Yagi-Uda Antenna

## Slide 21
Fig: Parametric sweeping for 8 elements
S parameter

## Slide 22
Fig: S parameter at 2.45 GHz
S parameter

## Slide 23
Fig: VSWR at 2.45 GHz
VSWR

## Slide 24
Fig: Far field analysis for 8 element Yagi-Uda Antenna6
Far-Field
The maximum far field gain achieved is 9.693 dBi.

## Slide 25
Fig: Gain vs Frequency curve
Gain vs Frequency
The gain is high at the desired frequency.

## Slide 26
Interpretation of Results
Wavelength value is changed to obtain desired output.
Parametric sweeping is applied .
8 element antenna has higher far field gain.
By using Boom results slightly shifts from the desired frequency.

## Slide 27
Application of the Design
The applications of the Yagi-Uda antenna are as follows:
Television reception in the VHF and UHF frequency ranges.
Amateur (ham) radio for long-distance communication.
Improve detection and tracking in radar systems.
Satellite communication for signal transmission and reception in ground stations
Wi-Fi signal enhancement in specific directions to improve coverage and reduce interference.

## Slide 28
Shortcomings/ Drawbacks of the Design
The drawbacks of the design of Yagi-Uda antenna are as follows:
The antenna has a narrow bandwidth, means it operates over a limited frequency range.
To achieve high gain, the antenna requires a large size with a long boom and multiple elements, making it bulky and difficult to install.
The design can become complex when additional directors are added.
The antenna is prone to noise and environment.

## Slide 29
Conclusion
The Yagi-Uda antenna is a highly effective design in wireless communication. Its simple structure, which includes a driven element and parasitic elements, allows for significant signal enhancement. This makes it a popular choice for applications like television reception, amateur radio, and radar systems. As technology continues to advance, there is great potential to improve the Yagi-Uda antenna's bandwidth and reduce its size for modern communication needs.

## Slide 30
References
1] H. Yagi and S. Uda, “Projector of the Sharpest Beam of Electric Waves,” Proc. Imp. Acad., vol. 2, no. 2, pp. 49–52, 1926, doi: 10.2183/pjab1912.2.49.
[2] C. A. Balanis, Antenna theory: analysis and design, Fourth edition. Hoboken, New Jersey: Wiley, 2016.
[3] C. A. Balanis, Modern Antenna Handbook. Somerset: Wiley, 2011.
[4] A. Zeghdoud, M. C. Derbal, and M. Nedil, “Gain Optimization of a Yagi-Uda Antenna using the Genetic Algorithm,” in 2019 IEEE International Symposium on Antennas and Propagation and USNC-URSI Radio Science Meeting, Atlanta, GA, USA: IEEE, Jul. 2019, pp. 1041–1042. doi: 10.1109/APUSNCURSINRSM.2019.8889003.
[5] R. Reddy and R. Swaminathan, “Directivity Improvement of 9-Element Yagi Uda Antenna by increasing director elements in comparison with 7-Element Yagi Uda Antenna,” in 2022 3rd International Conference on Intelligent Engineering and Management (ICIEM), London, United Kingdom: IEEE, Apr. 2022, pp. 561–564. doi: 10.1109/ICIEM54221.2022.9853131.

## Slide 31
[6] T. A. Nisamol, P. Abdulla., and K. K. Ansha, “Wideband Sub-THz Substrate lens Yagi- Uda antenna for 5G Communications and beyond,” in 2020 IEEE-HYDCON, Hyderabad, India: IEEE, Sep. 2020, pp. 1–5. doi: 10.1109/HYDCON48903.2020.9242679.
[7] A. Ali, H. Wang, and I. Park, “A Yagi-Uda Antenna Implemented with Solar Cells,” in 2024 IEEE International Workshop on Antenna Technology (iWAT), Sendai, Japan: IEEE, Apr. 2024, pp. 323–325. doi: 10.1109/iWAT57102.2024.10535854.
[8] R. K. Tanti, S. Warathe, and N. Anveshkumar, “Planar Yagi-Uda Antenna with Mirrored Ground Plane for WLAN,” in 2020 11th International Conference on Computing, Communication and Networking Technologies (ICCCNT), Kharagpur, India: IEEE, Jul. 2020, pp. 1–5. doi: 10.1109/ICCCNT49239.2020.9225278.
[9] D. Wang et al., “A Planar Quasi Yagi-Uda Antenna Designed For Liquid Crystal Based End-Fire Phased Arrays,” in 2021 IEEE Radio and Wireless Symposium (RWS), San Diego, CA, USA: IEEE, Jan. 2021, pp. 164–167. doi: 10.1109/RWS50353.2021.9360363.

## Slide 32
THANK YOU

## Slide 33: If any query